## Slide 1: Life Support Systems Working Together
By Matthew Katterman

## Slide 2: Life Support Systems working together

## Slide 3: Describing how life support systems work
Two definitions that describe life support systems
Synergistic – The interaction of elements that when combined produce a total effect that is greater than the sum of the individual elements, contributions, etc.
Synchronous – Occurring at the same time; coinciding in time; simultaneous

## Slide 4: Life Support Systems Questions sheet
Life Support Systems
Air Revitalization
Oxygen Generation
Atmospheric Control and Supply
Temperature and Humidity Control
Sabatier System
Water Recovery and Management System
Quick lesson on each of the systems, how they work.
There are a few questions to answer for each lesson. They are written on the sheet. Easy to answer.
Take a few minutes to write out the answers to the questions. Just need a few sentences, not much more.
Will talk about answers as you are writing them out.

## Slide 5: Air Revitalization System
Contaminants in cabin air space include carbon dioxide, particulates, dust, volatile organics.
Dust, particles and volatile organics removed by catalytic oxidation followed by chemical adsorption.
Carbon dioxide is removed by sorbent beds which are regenerated.
CO2 CO2
CO2 CO2
CO2 CO2
CO2 CO2
CO2
CO2
CO2
CO2 CO2
CO2 CO2
Cabin
Cabin
Air Revitalization
Air Revitalization
Sorbent Beds
Catalytic oxidation
Chemical Adsorption
Sorbents
Oxidation Adsorption

## Slide 6: Oxygen Generation System
Water is made up of hydrogen and oxygen atoms.
Creates oxygen from water, done by Electrolysis.
Splits up water into oxygen & hydrogen gases using electricity.
A battery, electrodes and electrolytes are needed to convert water into oxygen and hydrogen gases.
H2O
O2 H2
Water
Oxygen

## Slide 7: Atmospheric Control and Supply
What two gases make up most of the air we breathe?
Same proportions of nitrogen and oxygen mixed together in cabin.
  78 % Nitrogen, 21 % Oxygen
Nitrogen and oxygen are delivered from pressurized tanks.
The overall cabin pressure is controlled by the amount of Nitrogen provided to it.
N2 N2 O2 N2
N2 O2 N2 N2
O2 N2 N2 O2
N2 O2 N2 N2
O2 CO2
Breathe In Breathe Out
Oxygen
Nitrogen

## Slide 8: Sabatier System
Uses carbon dioxide recovered from Air Revitalization System.
Uses hydrogen made from the Oxygen Generation System.
Produces water for the Water Recovery system and Oxygen Generation system.
Methane is vented overboard but could be converted into hydrogen.
CO2 + 4H2
2H2O + CH4
Air Revitalization System
Oxygen Generation System
Water Recovery System
Vented overboard or can make hydrogen

## Slide 9: Temperature and Humidity Control
Maintain comfortable temperatures and humidity for the air cabins.
Temperature is controlled by velocity of air flow.
Water vapor is removed from the air and sent to the Water Recovery and Management system.
Air RevitalizationAtmospheric Control & Supply
Cabin Space
Velocity
Cabin Space Before
Air – Water Separator
Cabin Space After

## Slide 10: Water Recovery & Management System
Water is recovered from Temperature and Humidity Control System.
Water is generated by the Sabatier System.
Water is recovered from the urine of astronauts.
Water is recovered from baths, cleaning, hygiene activities.
Water Recovery System
Oxygen Generation System
Hydrogen
Sabatier System
Drinking
Urine Recovery
Baths, Hygiene
Humidity Control System